## Slide 1: Computer Memory
Unit 3

## Slide 2: MEMORY REPRESENTATION
The computer memory stores different kinds of data like input data, output data, intermediate results, etc., and the instructions.
Binary digit or bit is the basic unit of memory. A bit is a single binary digit, i.e., 0 or 1. A bit is the smallest unit of representation of data in a computer.

## Slide 3
1 bit = 0 or 1
1 Byte (B) = 8 bits
1 Kilobyte (KB) = 1024 bytes
1 Megabyte (MB) = 1024KB
1 Gigabyte (GB) = 1024 MB
1 Terabyte (TB) = 1024 GB

## Slide 4: MEMORY HIERARCHY

## Slide 5: CPU REGISTERS
Registers are very high-speed storage areas located inside the CPU. After CPU gets the data and instructions from the cache or RAM, the data and instructions are moved to the registers for processing. Registers are manipulated directly by the control unit of CPU during instruction execution. That is why registers are often referred to as the CPU’s working memory.
Since CPU uses registers for the processing of data, the number of registers in a CPU and the size of each register affect the power and speed of a CPU. The more the number of registers (ten to hundreds) and bigger the size of each register (8 bits to 64 bits), the better it is.

## Slide 6: CACHE MEMORY
Cache memory is placed in between the CPU and the RAM. Cache memory is a fast memory, faster than the RAM. When the CPU needs an instruction or data during processing, it first looks in the cache. If the information is present in the cache, it is called a cache hit, and the data or instruction is retrieved from the cache. If the information is not present in cache, then it is called a cache miss and the information is then retrieved from RAM.

## Slide 7: Primary memory
Primary memory is the main memory of computer. It is a chip mounted on the motherboard of computer. Primary memory is categorized into two main types-
Random Access Memory (RAM), and
Read Only Memory (ROM)
RAM is used for the temporary storage of input data, output data and intermediate results. The input data entered into the computer using the input device, is stored in RAM for processing. After processing, the output data is stored in RAM before being sent to the output device. Any intermediate results generated during the processing of program are also stored in RAM.
Unlike RAM, the data once stored in ROM either cannot be changed.

## Slide 8: Random Access Memory
RAM is used to store data and instructions during the operation of computer.
The data and instructions that need to be operated upon by CPU are first brought to RAM from the secondary storage devices like the hard disk.
CPU interacts with RAM to get the data and instructions for processing. RAM loses information when the computer is powered off. It is a volatile memory. When the power is turned on, again, all files that are required by the CPU are loaded from the hard disk to RAM. Since RAM is a volatile memory, any information that needs to be saved for a longer duration of time must not be stored in RAM.

## Slide 9: Types of RAM
Dynamic RAM (DRAM)
Static RAM (SRAM)

## Slide 10: Dynamic RAM (DRAM)
DRAM is the most common type of memory chip. DRAM is mostly used as main memory since it is small and cheap.
  DRAM must be refreshed continually to store information. DRAM gets its name from the refresh operation that it requires to store the information; otherwise it will lose what it is holding. The refresh operation occurs automatically thousands of times per second. DRAM is slow because the refreshing takes time.

## Slide 11: SRAM
SRAM chip is usually used in cache memory due to its high speed. It does not need constant refreshing and therefore is faster than DRAM.
SRAM is more expensive than DRAM, and it takes up more space. It stores information as long as it is supplied with power. SRAM are easier to use and very fast.

## Slide 12: Read Only Memory
ROM is a non-volatile primary memory. It does not lose its content when the power is switched off. ROM, as the name implies, has only read capability and no write capability.
ROM comes programmed by the manufacturer. ROM stores the data needed for the start up of the computer.
The ROM memory chip stores the Basic Input Output System (BIOS). BIOS provides the processor with the information required to boot the system.

## Slide 13
When the computer is turned on, the BIOS does the following things—
Power On Self Test (POST) is a program that runs automatically when the system is booted. BIOS performs the power-on self-test. It checks that the major hardware components are working properly.
BIOS setup program, lets the user set the many functions that control how the computer works.
Bootstrap Loader is a program whose purpose is to start the computer software for operation when the power is turned on. The bootstrap loader resides in the ROM.

## Slide 14: Types of Rom:
Programmable ROM (PROM)
Erasable Programmable ROM (EPROM)
Electrically Erasable Programmable ROM (EEPROM)

## Slide 15
PROM can be programmed with a special tool, but after it has been programmed the contents cannot be changed.
EPROM can be programmed in a similar way as PROM, but it can be erased by exposing it to ultra violet light and re-programmed.
EEPROM memories can be erased by electric charge and re-programmed.

## Slide 16: SECONDARY MEMORY
The secondary memory is also called the storage device of computer. In comparison to the primary memory, the secondary memory stores much larger amounts of data and information permanently. The data and instructions stored in secondary memory must be fetched into RAM before processing is done by CPU.
Example: Magnetic tape drives, magnetic disk drives, optical disk drives etc.

## Slide 17: ACCESS TYPES OF STORAGE DEVICES
The information stored in storage devices can be accessed in two ways—
1. Sequential access
2. Direct access

## Slide 18: Sequential access
Sequential access means that computer must run through the data in sequence, starting from the beginning, in order to locate a particular piece of data. Magnetic tape is an example of sequential access device.
If a magnetic tape consists of 80 records, to access the 25th record, the computer starts from first record, then reaches second, third etc. until it reaches the 25th record. Sequential access devices are generally slow devices.

## Slide 19: Direct Access Devices
Direct access devices are the ones in which any piece of data can be retrieved in a non-sequential manner by locating it using the data’s address. It accesses the data directly, from a desired location.
In a magnetic disk consisting of 80 records, to access the 25th record, the computer can directly access the 25th record, without going past the first 24 records.
Magnetic disks and optical disks are examples of direct access devices.

## Slide 20: MAGNETIC TAPE
Magnetic tape is a plastic tape with magnetic coating. It is a storage medium on a large open reel or in a smaller cartridge or cassette.
Data is recorded on tape in the form of blocks, where a block consists of a group of data also called as records. Each block is read continually. There is an Inter-Record Gap (IRG) between two blocks that provides time for the tape to be stopped and started between records

## Slide 21: Fig Magnetic Tape

## Slide 22: The features of magnetic tape are—
Inexpensive storage device
Can store a large amount of data
Easy to carry or transport
Not suitable for random access data
Slow access device
Needs dust prevention, as dust can harm the tape
Suitable for back-up storage.

## Slide 23: MAGNETIC DISK
Magnetic disk is a direct access secondary storage device. It is a metallic circular plate coated with magnetic oxide and encased in a protective cover. Data is stored on magnetic disks as magnetized spots. The presence of a magnetic spot represents the bit 1 and its absence represents the bit 0.
Magnetic disk is inserted into a magnetic disk drive for access. During reading or writing to disk, the motor of disk drive moves the disk at high speed.
Example hard disk, floppy disk etc.

## Slide 24: The features of magnetic disk are—
Cheap storage device
Can store a large amount of data
Easy to carry or transport
Suitable for frequently read/write data
Fast access device
More reliable storage device
prevent from dust

## Slide 25: OPTICAL DISK
Optical disk is a flat and circular disk which is coated with reflective plastic material that can be altered by laser light. Optical disk does not use magnetism. The bits 1 and 0 are stored as spots that are relatively bright and light, respectively.
The random access on optical disk is slower than that of magnetic disk, due to its spiral shape.
Example of optical disk are read-only optical disks and recordable optical disks.

## Slide 26: USING THE COMPUTER MEMORY
The computer starts using the memory from the moment the computer is switched on, till the time it is switched off. The list of steps that the computer performs from the time it is switched on are—
Turn the computer on.
The computer loads data from ROM. It makes sure that all the major components of the computer are functioning properly.
The computer loads the OS from the hard drive into the system’s RAM. CPU has immediate access to the OS as the critical parts of the OS are maintained in RAM as long as the computer is on. This enhances the performance and functionality of the overall system.
Now the system is ready for use.

## Slide 27
When you load or open an application it is loaded in the RAM. Since the CPU looks for information in the RAM, any data and instructions that are required for processing (read, write or update) is brought into RAM. To conserve RAM usage, many applications load only the essential parts of the program initially and then load other pieces as needed.
The CPU requests the data it needs from RAM, processes it and writes new data back to RAM in a continuous cycle. The shuffling(moving) of data between the CPU and RAM happens millions of times every second.
If the files are not saved to a storage device before being closed, they are lost.

## Slide 28
******THE END*******